## Slide 1: Arduino x Android 即時網頁繪圖
基於藍芽協定實現Arduino與Android間的通訊
並實作網頁呈現其資料的視覺化

## Slide 2: 目錄
1. Arduino
1.1. 光敏電阻
1.2. 藍芽模組
2. Android
2.1. Android 藍芽 API
    2.2. Graph View 3.0(java 繪圖函式庫)

## Slide 3: Arduino

## Slide 4: 光敏電阻(有兩種)
輸入pin腳:A0
第一種
兩隻腳

## Slide 5
第二種
三隻腳
輸入pin腳:A0
注意!!若讀取的數值無光時數值大，有光反而小時將S腳跟VCC交換接(可能為瑕疵品)
正常數值為0~1023

## Slide 7: ftp://student:1234@awin.cs.nchu.edu.tw
程式碼載點

## Slide 8: Arduino 程式碼
#include <SoftwareSerial.h>//載入軟體串列埠函式庫
#define sensorPin A0 //定義光敏電阻pin腳
SoftwareSerial BT(8,9);//定義藍芽串列埠pin腳
void setup() {
Serial.begin(9600);//設定基本串列埠的鮑率(訊號載波速率)
BT.begin(9600);//設定藍芽串列埠的鮑率(訊號載波速率)
}

## Slide 9: Arduino Code
void loop{
if(Serial.available()>0){ //監聽基本序列埠，如果有值的話
char re = Serial.read();//將資料讀入
switch(re){//做switch判斷(這邊用if判斷式的話為if(re==‘E’){})
case ‘E’://如果值是Ｅ的話
start();//呼叫start函示執行
break;
}
}

## Slide 10: Arduino Code
if(BT.available()>0){ //監聽藍芽序列埠，如果有值的話
char re = BT.read();//將資料讀入
switch(re){做switch判斷(這邊用if判斷式的話為if(re==‘E’){})
case ‘E'://如果值是Ｅ的話
start();//呼叫start函示執行
break;
}
}
}

## Slide 11: Arduino Code
void start(){
while(1){
Serial.print('s');
Serial.print(floatMap(analogRead(sensorPin),0,1023,0,5),2);//將analogRead所讀入的值做正規後印出
BT.print('s');
BT(floatMap(analogRead(sensorPin),0,1023,0,5),2);//將analogRead所讀入的值做正規化後經由藍芽送出
delay(30);//因為串列埠的傳輸速度有限，避免漏接所以停30毫秒
if(Serial.available()>0 || BT.available()>0){//監聽基本串列埠跟藍芽串列埠
if (Serial.read()=='Q') return;//如果接收到Ｑ則return 結束此函式
if(BT.read()==‘Q’) return;//如果接收到Ｑ則return 結束此函式
}
}
}

## Slide 12: Arduino Code
做資料正規化，將光敏電阻的值轉成0~5之間，避免在手機上呈現時超出螢幕
float floatMap(float x, float inMin, float inMax, float outMin, float outMax){
return (x-inMin)*(outMax-outMin)/(inMax-inMin)+outMin;
}

## Slide 13: Android

## Slide 14: Android
static ConnectedThread connectedThread;
public static final UUID MY_UUID = UUID.fromString(“00001101-0000-1000-8000-00805F9B34FB");
static BluetoothAdapter btAdapter;

## Slide 15: BluetoothAdapter btAdapter
private void getPairedDevices() {
devicesArray = btAdapter.getBondedDevices();
if (devicesArray.size()>0){
for(BluetoothDevice device:devicesArray){
pairedDevices.add(device.getName());
}
}
}

## Slide 16: BluetoothAdapter btAdapter
private void startDiscovery() {
// TODO Auto-generated method stub
btAdapter.cancelDiscovery();
btAdapter.startDiscovery();
}

## Slide 17: BluetoothAdapter btAdapter
private void getPairedDevices() {
deviceArray = btAdapter.getBondedDevices();
if(deviceArry.size>0)
for(BluetoothDevice device:devicesArry){
pairedDevices.add(device.getName());
}
}

## Slide 18: BluetoothAdapter btAdapter
@Override
public void onItemClick(AdapterView<?> arg0, View arg1, int arg2, long arg3) {
// TODO Auto-generated method stub
if (btAdapter.isDiscovering()){
btAdapter.cancelDiscovery();
}

## Slide 19: BluetoothAdapter btAdapter
if(listAdapter.getItem(arg2).contains("(Paired)")){
BluetoothDevice selectedDevice = devices.get(arg2);
ConnectThread connect = new ConnectThread(selectedDevice);
connect.start();

## Slide 20: BluetoothAdapter btAdapter
}else {
Toast.makeText(getApplicationContext(), "device is not paired", 0).show();
}
}

## Slide 21: ConnectThread
private final BluetoothSocket mmSocket;
private final BluetoothDevice mmDevice;
public ConnectThread(BluetoothDevice device) {
BluetoothSocket tmp = null;
mmDevice = device;

## Slide 22: ConnectThread
try {
tmp = device.createRfcommSocketToServiceRecord(MY_UUID);
} catch (IOException e) { }
mmSocket = tmp;
}

## Slide 23: ConnectThread
public void run() {
btAdapter.cancelDiscovery();
try {
mmSocket.connect();
}

## Slide 24: ConnectedThread
static class ConnectedThread extends Thread {
private final BluetoothSocket mmSocket;
private final InputStream mmInStream;
private final OutputStream mmOutStream;
public ConnectedThread(BluetoothSocket socket) {
mmSocket = socket;
InputStream tmpIn = null;
OutputStream tmpOut = null;

## Slide 25: ConnectedThread
try {
tmpIn = socket.getInputStream();
tmpOut = socket.getOutputStream();
}

## Slide 26: ConnectedThread Reader
StringBuffer sbb = new StringBuffer();
public void run() {
byte[] buffer;
int bytes;
while (true) {
try {sleep(20);}
buffer = new byte[1024];
bytes = mmInStream.read(buffer);
mHandler.obtainMessage(MESSAGE_READ, bytes, -1, buffer).sendToTarget();
}

## Slide 27: ConnectedThread Writer
public void write(String income) {
try {
mmOutStream.write(income.getBytes());
for(int i=0;i<income.getBytes().length;i++)
Log.v("outStream"+Integer.toString(i),Character.toString((char)(Integer.parseInt(Byte.toString(income.getBytes()[i])))));
try {
Thread.sleep(20);}